## Slide 1: Parks on the Air (POTA) Program Overview
KEVIN CULP, KZ3L AND JACK KIBELBEK, N8EU
Presented to the NEWARK AMATEUR RADIO ASSOCIATION
APRIL 16, 2022

## Slide 2: INTRODUCTION
Presenters
  Kevin Culp, KZ3L
    Licensed since 1983 – Amateur Extra Class since 1986
    Primarily a CW & portable op
    Currently the Ohio POTA Mapping Coordinator
    32-year active duty Air Force career + civil service – Engineering / Occupational Health
  Jack Kibelbek, N8EU
    Licensed since 1969 – Amateur Extra Class since 2018
    Primarily a CW op + portable QRP
    Retired pediatrician

## Slide 3: INTRODUCTION
What is Parks on the Air (POTA)?
  A FUN, FUN activity!  NOT a contest
  Promotes portable amateur radio operations & enjoyment of our parks
  Spend more on-air time (home or portable)
  An awards program
  Encourages communications “readiness”
  Enjoy “field day” any day of the year!
  No HOA restrictions or local electrical noise – HUGE DIFFERENCE!
  Combine with other hobbies—disc golf, fishing, camping, hiking, boating, etc.

## Slide 4: INTRODUCTION
Origin: ARRL’s National Parks on the Air (NPOTA) – 2016
  Celebration of USA’s 100 year National Park history
  POTA program began shortly thereafter
Started in US, now International
  >9,000 parks in the U.S.
  Numerous countries being added
  Activators often feel like rare DX, even CONUS!

## Slide 6: TERMINOLOGY
Park (a.k.a. “reference area”)
  Federal- or State-owned and operated entity
  Parks, sites, forests, preserves, refuges, wildlife areas, trails, etc.
  MUST be listed in the POTA database to count (e.g. K-1940)

## Slide 7: TERMINOLOGY
Activation
  Station completes 10+ QSOs in any 24-hour UTC day from the park
  Distinct QSO = band + mode + call
  No specified exchange! ANY QSO counts (even contest QSOs)
  Simplex only (except satellite)
  No limit on # activations at a park
Activator
  A station which activates a park
  Must be located in the park (duh!)
  Trail: within 100’, on public land

## Slide 8: TERMINOLOGY
Hunter
  A station which calls an activator
  An activator can ALSO be a hunter; see below
Park-to-Park
  QSO between two parks
Late Shift
  Between the hours of 0000 and 1200 UTC

## Slide 9: HUNTING A PARK
Most common way to participate
Without hunters, the entire program would FLOP!
Simplest way to learn about POTA
Call from anywhere, anytime (home QTH, mobile, another park)
Build list of parks and earn awards quickly!
Awards program is automatic – only activators submit logs to POTA
Get started: Register at http://pota.app

## Slide 10: HUNTING A PARK
Check spots page--Best way to find activators (pota.app)
Tune up on empty frequency
Listen for call, QSO style & cadence
Announce your call 1x after CQ, QRZ?
Spot the activator on pota.app)
Breaking through pile-ups:
  On CW, never zero-beat! TX slightly off freq (0.05-0.1 kHz)
  On SSB, it’s tough… tail-ending is discouraged. Compression helps

## Slide 11
Spotting page
Filter by band & mode
Sort by freq or time
Log into your account to spot activators
Watch comments
  “Last heard…”
  QRT
  Sig reports
  Less common modes (FT4, FT8, etc.)
Refreshes automatically

## Slide 12: ACTIVATING A PARK
Register at http://pota.app
Read guides & FAQs at http://parksontheair.com
Selecting a park
  Look on http://pota.app
  Research geographic boundaries
    Ohio: DNR GIS or Park Web Site https://gis.ohiodnr.gov/MapViewer/?config=ODNRLands
  Know park rules (hours, limitations, access, parking, trails, etc.)
    Check the official park web site https://ohiodnr.gov/go-and-do/plan-a-visit/find-a-property/find-a-property-search

## Slide 17: ACTIVATING A PARK
What’s your style?
  Extremes:
    All the comforts of home – lodge/cabin?
    Hike-in activation
  Very common:
    Bring your own shelter, tent, or canopy
    Use existing infrastructure
    Set up your own table & chair
    Activate from inside the car

## Slide 21: ACTIVATING A PARK
Where in the park?
  Use maps, Google Earth, etc.
  Trees vs. open field vs. parking lot
  Facilities (you know what we mean)
  Other park users
  Elevation
  The view

## Slide 22: ACTIVATING A PARK
Before you go
  Do your planning!
  Check weather, prop forecast, etc.
  Document Park # and County
  Inventory and triple-check equipment
    Dead battery? Missing coax?
  Schedule your activation on http://pota.app (optional)
    Reverse Beacon Network can help to spot you – CW or Digital
    Hunters can look for you

## Slide 23: ACTIVATING A PARK
Select a band: All bands are fair game (incl WARC)
Spot Yourself on http://pota.app
Calling CQ
  Listen, then QRL? Is this freq in use?
  “CQ POTA… from [call] at Park K-####”
Typical Exchange
  Call, state, and RS(T) report
  There is no required exchange
Tradition: Give priority to “Park to Park” (or “P2P” on CW), “QRP”, and “Mobile”
CALL OTHER PARKS! (P2P)

## Slide 24: ACTIVATING A PARK
Logging
  Date & Time (UTC)
  Your call
  Their call
  Band (freq not req’d for POTA, but helpful for other logs like QRZ and LoTW)
  Mode
  Their park # (optional)
    Avoid dupes if activating multiple parks

## Slide 25: AFTER ACTIVATION
Repack/refresh/recharge
Leave park better than you found it
Finalize log & submit to POTA
  Triple check logs before sending
  ADI File (ADIF) format ONLY
  File name = call@K-####-yyyymmdd
    Add state if park spans multiple
  Send to K#@parksontheair.com (# = your call sign #)
  Coordinators are volunteers – might take 3-4 wks for log to appear in stats

## Slide 26: PORTABLE EQUIPMENT
Radio
  HF most common
  May use VHF/UHF if desired
    No repeaters
    Satellite/ISS allowed
  Adjust to your operating style
    Hiking in? Go lite!

## Slide 27: PORTABLE EQUIPMENT
Power
  Anything goes, even available 110AC
  Gas generator probably excessive
  Batteries most common
    LiFePO4 light w/~80% usable capacity
    Rough rule of thumb: 5Ah/hr/100W power setting
    12 Ah LiFePO4 good for ~1:45 - 2 hrs
  Cut power in half = only 0.5 S-unit loss
  Measure use w/in-line power meter
  Anderson PowerPoles a good choice

## Slide 28: PORTABLE EQUIPMENT
Antennas
  NUMEROUS options!
  Adapt to location and style
  Consider support structure (self-supporting, trees, in car)
  Low power? Resonant is best choice
  Common choices:
    End-Fed Halfwave or “Random”
    Dipole / inverted vee
    Multiband vertical

## Slide 29: PORTABLE EQUIPMENT
Antennas
  Common choices (cont.):
    Coil-loaded, such as the Wolf River Coil products
    Hamsticks (don’t underestimate!)
Feedline
  Coax most convenient
  Short runs (<50’) = low loss
  Feedline choke may help w/stray RF
  Not always needed (feed directly from radio)

## Slide 30: PORTABLE EQUIPMENT
Cases / transportation
  Hard case
  Soft case / backpack
  Economize!
  Hiking? Small kit can fit in a fanny pack!
All other accessories
  Cables, connectors, spare cables, tools, tape, zip ties, headphones, mic, key
Personal care items
  1st aid kit, bug spray, sun screen, gloves/hat, food, water, towels

## Slide 31: PORTABLE EQUIPMENT
Pro tips
  Arborist throw line, rope, and weight – great way to get antenna in a tree (50-70’)
  Use kite winders (“figure 8”) to store wire antennas
  “Over-under” method for coax, bundles of radials, etc.

## Slide 32: LOGGING SOFTWARE
Your choice!
Be sure it generates ADI file with needed fields
Common Options:
  N3FJP’s AC Log (Windows)
  HAMRS (All platforms)
  N1MM Plus (Windows)
  RUMLog (Mac/iOS)
  Custom spreadsheets
  FLE - Fast Log Entry
  ADIF Master (great to check ADIFs)

## Slide 33: AWARDS
Automated – based on activator log
Numerous – for activators & hunters
  # parks, # activations, # park-to-parks, repeat activations/hunted, “kilo,” multiple parks/day, 10-band, etc.
  Thresholds start early and build (10, 20, 30, 40, 50, 75, 100, 500, 1000…)
Download from pota.app
May take 1-4 weeks to appear
Excellent progress tracker

## Slide 35: SPECIAL TOPICS
Handling Nets and QRM
  Always take the high road!
  No one “owns” a freq, but be a good ambassador for the program
  Deliberate QRM does happen
Contests: Can’t beat ‘em? Join ‘em!
  Or go to WARC bands or other modes
  http://contestcalendar.com
Always submit logs! Hunters want parks

## Slide 36: SPECIAL TOPICS
Multi-Op activations
  Share the mic or key
    Ops all get POTA credit
    Follow FCC ID rules
    Submit separate logs
  Simultaneous
    Operate on different bands
    Separate antennas from each other as far as practical
    Use band-pass filters

## Slide 37: Special Topics
Multi-Park activations
  “two-fer,” “three-fer,”…
  Park-within-a-park
  In a park and w/in 100’ of trail
  Any combination of above
  Every QSO counts for each park
  Submit separate logs for each park

## Slide 38: GETTING STARTED
Register at http://pota.app
Visit http://parksontheair.com
  Read FAQs and guides
  Watch videos
Practice hunting & listen to other activators
Join POTA Facebook Group and Slack channel – great communities!
  See info on http://parksontheair.com
HAVE A HAM GOOD TIME!!!

## Slide 39: Questions?
KEVIN CULP, KZ3L – KZ3L@ARRL.NET
JACK KIBELBEK, N8EU – JACK45458@YAHOO.COM